## Slide 1: THE “INs AND OUTs” OF ALLEYS FOR THE CITY OF HOUSTON

## Slide 2
CHAPTER 40-ARTICLE XV HOUSTON CODE OF ORDINANCES Ord: 99-379
Code of Ordinances 40-340 through 40-346
ALLEY
  Access easement across the rear lot
  Must connect to two public streets
PRIVATE ALLEY
  Not Platted
    Essentially a driveway on private property
PUBLIC ALLEY
  Dedicated ROW-Platted (shown on recorded plats)
    PRIVATE ACCESS (Residential Only)
    PUBLIC ACCESS
    Not all dedicated alley ROW has been accepted by City for Maintenance

## Slide 3
PRIVATE ALLEY
Not platted
  Private Access by Driveway
  Connection to Public Street Only at Ends
  Application for Access as a Driveway
  Permit at 3300 Main Street, Traffic Section
    Application and Driveway approach detail

## Slide 4
PUBLIC ALLEY PRIVATE ACCESS (Residential)
IMPROVED
Asphalt
Concrete
Gravel/Shell (6 inch compacted min.)
V-section or culvert
Low Impact Design
Follow city design standard
  12-ft width min. paving if ROW >15 feet
  8-ft width min. paving if ROW <15 feet
NON-IMPROVED
Have not had any improvements
Drivable – no paving req.
Minor repairs – limited spot repairs 3’x3’ / block

## Slide 5
Alley Improvement
Spot Repair

## Slide 6
PRIVATE ACCESS ALLEY Typical Design

## Slide 8
PUBLIC ALLEY PRIVATE ACCESS PERMITTING
3300 Main
STEP I - Plans
  Site Plan (dimensioned)
    Alley width
    Garage Door set back from property line (20-ft min. clearance from garage to far side of alley)
    10’ drivable surface beyond driveway for exiting
  Pictures of existing alley
STEP II - Application
  - 3300 Main, Traffic Section
  Provide Plans and No
    Objection Letter
Permits
  Driveway
  Sidewalk
No Objection Letter
  Request to City Engineer’s Office—Attn: Richard Smith
  Review = 2 weeks for verification of conditions (map or site visit)

## Slide 9
20-ft alley cross clearance
10-ft clear driving area beyond edge of driveway

## Slide 10
PUBLIC ALLEY PUBLIC ACCESS (Commercial)
Asphalt
Concrete
V-section or culvert drainage
Follow city design standard
V Section Typical Design

## Slide 11
Asphalt V Section
Gravel

## Slide 12
PUBLIC ALLEY PUBLIC ACCESS PERMITS
Plans (Engineered Design)
  Survey
  Alley Plan and Profile
    Provide No Objection Letter with Plan set
Application
  3300 Main, Traffic Section
  Provide Plans Permits
  Driveway
  Sidewalk

## Slide 13
PUBLIC ALLEY ALLEY IMPROVEMENT PERMIT –
611 Walker
Plans
  5 Sets (24” x 36”)
  Utility Approvals
  Bound copies provided for Thursday walk through
  Approved plans sent for signature and scanning
  Pickup following Tuesday
Permits
  Street Cut
  Storm and Paving

## Slide 14
Alleys with Culvert Drainage System

## Slide 15
Alleys with Drainage Considerations

## Slide 16
ENCROACHMENTS-VIOLATIONS
EXISTING > 1 YEAR
  Property matter between Homeowners
NEW HOME CONSTRUCTION
  Red Tag by Code Enforcement unless they have completed all permitting requirements
NEW < 1 YEAR
  Red Tag by
    Street ROW Inspectors

## Slide 17
OTHER
ALLEY DRAINAGE
  Is not to drain onto adjacent property
  Storm water to drain along alley into drainage facilities or intersecting street.
  Is not to be the primary drainage for abutting development
MAINTENANCE
  City does not maintain unless constructed to street standards
  City does have and maintain utilities within alleys
  78 existing alleys
JOINT REFERRAL
  Abandonment or sale of alley can be requested when underlying fee owner is known
Website:
http://documents.publicworks.houstontx.gov/document-center/alleys-maintained-by-the-city/index.htm

## Slide 18
EXAMPLES
Accessible Alley
Alleys Requiring Improvement

## Slide 20
NEIGHBORHOOD PROTECTION Ord: 10-451(b) (10) & 10-341 © (15)
Investigates weed, debris, trash complaints
Adjacent property owners are notified of violation(s)
Lien assessed on non-compliant properties
High visibility/hazard locations cut by our Special Projects Team
Alley obstructions are referred to Structural

## Slide 21
SOLID WASTE
Adopt - A- Container Program
  Non-profit organizations
    May request large bulk containers for weekend neighborhood cleanup campaigns.
    Requests must be sent to the SWMD in writing at least 14 days prior to the anticipated cleanup date.
    Bulk Containers are provided on a “first come, first serve” basis
    Containers are delivered on Friday and collected on Monday.
    Only non-profit organizations and civic organizations coordinating a neighborhood cleanup campaign are eligible to sponsor bulk containers.
    For more information, call 3-1-1.

## Slide 22
MOST COMMON
MISTAKES AND COMPLAINTS
Drainage
  Muddy and rutted alley
  Water flow or standing water
Encroachments
  Buildings into alley
  Fences into or across alley
Landscaping
  Trees
  Maintenance of alley vegetation
Illegal Construction
  Working without a permit in City ROW

## Slide 23
CONTACTS
Office of City Engineer Richard Smith 832-394-9137 Lagnesh Varshney 832-394-9100
Note:
Effective June 2011, Code Enforcement and Office of City Engineer will be located at:
Houston Permitting Center: 1002 Washington Ave.